## Slide 1: DDD Mode Pacemaker
COMPSYS 303 Assignment 2
Savi Mohan, Mark Yep (Group 3)

## Slide 2: Introduction
DDD Mode Pacemaker
  Senses from both atrium and ventricle
  Paces both atrium and ventricle
  Support both Triggered and Inhibited pacing
  SCCharts
  Synchronous state chart software
  Simplifies development of complex concurrent systems
  Nios II Processor
  Platform for embedded systems
  The Processor is programmed onto FPGA device

## Slide 3: SCCharts Design
Timers
  Six intervals measured with timers
  Each timer represented by two regions in SCCharts
  Concurrently running
  Interact to correctly pace the heart
  Logic
  Additional state charts synchronise timers to get DDD timing diagram
  Also handle inputs and outputs
  Internal signals link the timers to the logic state charts

## Slide 5: SCCharts Features
State charts are developed through writing statements
Graphical diagrams are generated automatically
Can then compile into C code

## Slide 6: Altera Nios II Project
Timers
  Implemented with alt alarms
  Timers for pacemaker intervals
  Timers for pacemaker signals length
  Debounce timers for LEDs and buttons
  Inputs
  Buttons
  UART signals from virtual heart emulation
  Outputs
  LEDs

## Slide 7: Linking SCCharts and Nios II
SCCharts compiles to C code
C code and header file included in Nios II project
Inputs to SCCharts
  Vsense and Asense
  Timeout flags for timers
  Outputs from SCCharts
  Vpace and Apace